## Setup for use of parallel port under Python
Update August 2104: a Linux live DVD is now available to allow one to experiment and use the programs presented here without installation to one's computer.
See Live Linux Distro for Using Printer Port with Electronics
Check to see if /dev/parport0 exists with your file manager. If it isn't there then "sudo modprobe ppdev". This is default with most 2.6 and later Linux kernels. Now it should be present.
To have ppdev loaded on bootup (if you had to load it) do the following with your favorite text editor:
$ sudo leafpad /etc/module
Add "ppdev" save and close.
Next we must gain access to the parallel port by removing module lp:
$ sudo rmmod lp
Open the following with a text editor such as leafpad:
$ sudo leafpad /etc/rc.local
Add before 0: "rmmod lp" save and close.
That will remove module lp on bootup.
Next one will still need to be a member group lp if it's there:
$ sudo adduser whoever lp
Even if the module is removed to allow access to the parallel port one must still be a member of group lp or operate as root.
Reboot the machine log back in.
## Issues with the software
First issue is when pyparallel-0.2.zip is downloaded from www.sourceforge.com and unzipped the install will fail.
The software is just plain screwed. I managed to find the correct setup file elsewhere and got it to work and include that in my corrected version for download from my website. Do the following from a terminal (must have internet connection):
$ mkdir pport
$ cd pport
$ wget http://www.bristolwatch.com/pport/tar/pport.tar.gz
$ tar -zxvpf pport.tar.gz
Then:
$sudo python setup1.py install
## Short Introduction
Note the PC port doesn't include a 5-volt power supply and one must use an external supply. Don't exceed 5 volts!
With the 8 LEDs connected start python on the command line and enter the following:

>>> import parallel
>>> p = parallel.Parallel() #open LPT1
>>> p.setData(0x55)
Assuming one has 8 LEDs connected to the data port pins 2-9 (through a resistor to ground) 4 LEDs should be on. (D0, D2, D4, D6) The data port value can be from 0 to 255 but will be in binary format on the LEDs.
It's easy to use idle for python programming if one is using Debian. Ubuntu, etc. Otherwise open the following with a text editor such as leafpad or beaver:
$ leafpad count.py
This will produce an empty file - copy and past the following code then save as count.py in the pport directory you created earlier:

#!/usr/bin/env python

import parallel
import time

p = parallel.Parallel()

# Count 0-255 binary on 8 LEDs

for var in range(0,256):
    p.setData(var)
    print var
    time.sleep(.5) #delay 500 mSec.

p.setData(0x00) # turn LEDs off

print "Good by!"

exit
Save and exit the editor.
Type "ls" and make sure the file count.py can be seen. Then type the following:
$ python count.py
The program will print the count from 0 to 255 on the terminal and display the value in binary on the 8 LEDs. When reaching 255 the program will turn all the LEDs off, print "Good by!" and exit the program.
Notice the first line "#!/usr/bin/env python". This tells the system to execute the file using python. To do that we must make file count.py executable:
$ chmod +x count.py
Now one doesn't have type python simply:
$ ./count.py
One can even rename the file count.py to leave off the .py:
$ mv count.py count
Then type ./count and it will work as before.
If one wants to execute "count" anywhere do the following:
$ sudo mv count /usr/local/bin
Then type "count" on any terminal and the program will run.